## Slide 1: ZOO QKERAS VS LARQ
Presenter name

## Slide 2: Agenda
#
Network Description
#
Weights
#
Saved Network
#
Test and Results

## Slide 3: Network Description 1/2
  Tested Network:
  From larq.zoo
    QuickNetSmall
    QuickNet
    QuickNetLarge
  From larq.literature
    AlexNet

## Slide 4: Network Description 2/2
All of them are trained on the ImageNET dataset
Details about the hyperparameters used can be found in the larq zoo github repository
We performed a 1 to 1 translation of the networks from larq framework to qkeras framework and reuse the weights trained in larq

## Slide 5: Weights
The weights used to run the test can be downloaded here:
  QuickNet
    https://github.com/larq/zoo/releases/download/quicknet-v1.0/quicknet_weights.h5
  QuickNetSmall
    https://github.com/larq/zoo/releases/download/quicknet-v1.0/quicknet_small_weights.h5
  QuickNetLarge
    https://github.com/larq/zoo/releases/download/quicknet-v1.0/quicknet_large_weights.h5
  AlexNet
    https://github.com/larq/zoo/releases/download/binary_alexnet-v0.2.0/binary_alexnet_weights.h5
  BiRealNet
    https://github.com/larq/zoo/releases/download/birealnet-v0.3.0/birealnet_weights.h5
  Binary_resnet_e18
    https://github.com/larq/zoo/releases/download/resnet_e-v0.1.0/resnet_e_18_weights.json

## Slide 6: Random Generated Test
Here the steps to compare ”how well” qkeras network replicates the larq ones:
  Generate a dataset with the same shape of the ImageNET (None, 1, 224, 224, 3) composed of random integer value {0, 254} to simulate images
  Run the inference of both version of the network (larq and qkeras)
  For each sample compute mean of the MSE element by element of the two results
  Count how many times the two network gives different class prediction

## Slide 7: ImageNET Test
Here the steps to compare ”how well” qkeras network replicates the larq ones:
  Load 2000 sample from the imageNET dataset
  Resize the images to (224,224,3)
  Count how many times the two network gives different class prediction

## Slide 8: Results
NETWORK | RANDOM DATASET – 100 samples |  | IMAGENET DATASET – 2000 samples | 
 | Mean MSE | Misclassification | Mean MSE | Misclassification
QuickNet | 5.6e-05 | 0 | 0,00014 | 
QuickNet Small | 0.0 | 0 | 0,00003 | 
QuickNet Large | 6.9e-18 | 0 | 0,00023 | 
AlexNet | 0.0 | 0 |  | 
BiRealNet | 8.4e-05 | 6 |  | 
Binary ResNet e18 | 0.0 | 0 |  |